EET K258 Lab #5
Mixed signal Breadboard
Name: ____________________	Last edit: 15 Feb 2019

Safety: This introductory lab poses no safety hazards. The power supply has a low output voltage and includes a current limiting feature. There are no storage elements such as capacitors or inductors. Nonetheless, later labs will present significant hazards to life and limb. With this in mind, we will strive to develop habits that will keep us safe in the future. Specifically:
- There will be a lab instructor observing your activities at all times.
- Remove all watches, rings, and exposed necklaces.
- Keep your lab work area clean.
- This lab is comprised on dozens of individual steps. To help you keep track of where you are, add a check mark as you complete each step.
- Observe all of the “Stop, do not proceed until your lab instructor inspects...” directions. This allows someone to double check your wiring and verify you are ready for the experiment.
- You can expect your instructor to ask you questions about the portion of the experiment you are going to perform. Most questions will be centered on applications of the fundamental concepts and equations. You may be asked to collaborate with your classmates before proceeding.
Equipment:
PC	Arduino nano microcontroler
Keysight E3631A DC Power Supply	Fluke 115 digital multimeter
2ea Breadboard	2ea 1 kΩ resistors
2ea 2.2 kΩ resistors	4ea 10 kΩ resistors
2ea 390 kΩ resistors	2ea 500 kΩ potentiometer
2ea LM741 op-amp	2ea PN2222A transistor
2ea 1 uF electrolytic capacitor	2ea 0.1 uF film capacitor

Objective:

- Breadboard a mixed signal circuit
- Explore operation of the Arduino PWM
- Explore Arduino string operations.
Deliverables:

30 points: an exact functional copy of the breadboard
10 points: complete discussion questions attached to this document
Chalk talk:

- Download the code, pictures, and schematic from Blackboard.
- Operation of the Arduino PWM.
- Low pass filter
- Common collector (emitter follower) amplifiers
- non-inverting op-amp
## Questions:
1. (1 pt) describe the output signal from the 741 op-amp:

   A) Frequency =

   B) Amplitude =
2. (2 pts) Describe the signal as measured at the output of the Arduino D11 pin.

   A) Frequency =

   B) Amplitude =

   C) How can this be transformed into a sinusoid signal?
3. (1 pt) What is the time constant of the low pass filter formed by R1 and C1? How does this relate to the previous two questions?
4. (1 pt) What is the purpose of capacitor C2?
5. (1 pt) Research non-inverting op-amp. What is the gain of the 741 amplifier stage?
6. (1 pt) Research the term Direct Digital Synthesis. Explore the various code files associated with this project as provided by the instructor. One of those files contains a large look-up table. What is contained in this table?
7. (3 pts) Research C programming. What is contained in”

   A) a .h file?

   B) a .cpp file?

   C) a .ino file?
Procedure:

1. Joystick and LED:

   ____	Interface a 2-axis analog joystick to the Arduino such that:

   ____	power and ground supplied by the Arduino’s 5 VDC USB connection

   ____	vertical applied to A0

   ____	horizontal applied to A1

   ____	Install the tri-colored LED with series resistors such that:

   ____	Red on D10

   ____	Green on D11
  ____	Blue D12
2. Construct a program with the following attributes:

   ____	the raw joystick variables are scaled to floats such that

   -1 <= joy_LR <= 1

   -1 <= joy_UD <= 1

   ____	the scaled joystick variables are displayed in the serial monitor with the
   following format:

   LR = X.XX, UD = X.XX

   Hint: research the difference between Serial.println( ) and Serial.print( )

   ____	the green LED is on when:

   -0.75 < joy_LR < 0.75 AND -0.75 < joy_UD < 0.75

   ____	the blue LED will turn on when:

   -0.75 <= joy_LR OR joy_LR >= 0.75
  ____	the red LED will turn on when:

  -0.75 <= joy_UD OR joy_UD >= 0.75
3. Add a buzzer to the program:

   ____	The buzzer will beep 3 times from within a for loop whenever the joystick transition out	of the left / right 0.75 window.

   Hint:

   A) Use the Arduino tone( ) function.

   B) Use the static qualifier to remember the previous value between loop iterations.

   ____	The buzzer will beep 4 times from within a while loop whenever the joystick transition	out of the up / down 0.75 window.

   ____	The buzzer will beep beep once when the joystick returns to the 0.75 window.
4. Clean up:

   ____	The joystick and try color LED will be a permanent fixture in future lab experiments.	Clean up the breadboard so that:

   ____	Assemble (solder) the Arduino Micro if you have not already done so.

   ____	Power the breadboard rails via the Arduino’s GND and 5 VDC pins.

   ____	The joystick and LED are placed on the far side left side of the breadboard	leaving a gap for future experiments.

   ____	LED series resistors are cut and stood upright (gold band on short leg)

   ____	Wires are run underneath the Arduino micro (in the trench).

   ____	(10 pts) Your construction is approved by your lab instructor.
5. Finish:
  (40 pts) Push the finished lab to github.com.